## Slide 1
MID REVIEW
TapMap
An Autonomous Percussive Defect-Mapping Rover
Robotic automation of ASTM-style tap testing — finds hidden hollow tiles and
concrete delamination, and turns them into a spatial defect map.
GROUP
11 · CSE-AI · Batch A
DOMAIN
ROS 2 · Robotics · Deep Learning
BUDGET
₹3,000 of ₹6,000 cap
Notes: Open with the one-line pitch: inspectors find hollow tiles by tapping and listening. TapMap does the tapping, the listening, and the mapping — autonomously.

## Slide 2
THE PROBLEM
Structural defects you cannot see
A floor tile, façade cladding or concrete deck can look perfectly intact while the adhesive layer beneath it has failed — leaving a hidden air gap called debonding or delamination.
Façade tiles fall
Detached cladding drops from buildings onto pedestrians — a recurring cause of injury and death in Indian cities.
Bridge decks fail
Rebar corrodes, expands, and cracks the concrete cover from inside. Delamination is the earliest visible symptom.
Homes crack
Hollow floor tiles pop, crack under load, and require full re-laying instead of a spot repair.
SOUNDING PHYSICS
Bonded tile
sharp "tick" · ~2 kHz · fast decay
Debonded tile
AIR GAP
dull "thud" · ~500 Hz · slow decay
The air gap changes the acoustic response.
That difference is what TapMap measures.
Notes: Emphasise that percussion sounding is an accepted NDT method — ASTM D4580 — not something we invented. We are automating an existing accepted practice.

## Slide 3
EXISTING SOLUTIONS
Two options today — both inadequate
MANUAL TAP TESTING
An inspector strikes the surface with a rod and judges the sound by ear.
Subjective
depends entirely on one person’s ear and experience
No record
no map, no coordinates, no repeatable evidence
Slow & tiring
fatigue degrades accuracy over a large area
Not repeatable
two inspectors, two different results
COMMERCIAL NDT INSTRUMENTS
GPR, infrared thermography, ultrasonic array scanners.
Cost
several lakh rupees per instrument
Skill
requires a trained operator to interpret
Access
out of reach for municipal bodies and housing societies
Manual
still hand-held — no autonomous area coverage
The gap: nobody has cheaply robotised percussion sounding with spatial mapping. TapMap costs ₹3,000.
Notes: This slide sets up the gap our project fills. Expect a question on why not thermography — answer: cost, and it needs a thermal gradient which indoor floors rarely have.

## Slide 4
CONCEPT OF OPERATION
How the robot works
Placed at any corner of a room. Everything after that is autonomous — including discovering the size of the area it must scan.
1
EXPLORE
Drives the room boundary using the ToF sensor to discover the scan rectangle
2
CALIBRATE
10 taps on a known-good area learn this surface’s baseline signature
3
COVER
Boustrophedon (lawnmower) grid generated over the discovered area, 8 cm spacing
4
TAP
Stop → settle 400 ms → 30 ms solenoid strike → 100 ms gated audio capture
5
CLASSIFY
MFCC features → CNN → bonded / debonded with a confidence score
6
MAP
Tap stamped at tapper_link pose into a live occupancy-grid heat map
7
RETURN
Drives back to origin; reports its own position error as an accuracy audit
8
REPORT
Refined defect regions exported as a PDF inspection report
Notes: Stress step 1 and step 7. Step 1 is the autonomy claim; step 7 is how we prove the map is trustworthy.

## Slide 5
PHASE 1 — EXPLORE
The robot finds its own workspace
No dimensions are typed in. Using a single forward-facing ToF sensor, the rover itself acts as the pan mechanism: it drives, sees a wall, turns on gyro heading, and drives again.
A
Placed at a corner; odometry zeroed, map frame anchored here
B
Drives forward until ToF < 15 cm → wall found → records length L
C
Rotates 90° closed-loop on fused gyro heading
D
Drives until the next wall → records width W
E
Returns to origin; the L × W rectangle becomes the scan area
DISCOVERED RECTANGLE
start
L
W
Phase 2 then fills this rectangle with the
tap grid — 8 cm spacing, ~150 taps per m².
ROS 2 impact: a second action server /discover_area feeding /scan_area, sequenced by a mission-planner state machine.
Notes: Expected question: what if the room is not rectangular? Answer: v1 assumes a convex rectangular workspace and a max_area safety parameter; non-convex perimeter tracing is future work.

## Slide 6
HARDWARE IMPLEMENTATION
Hardware architecture
Thin real-time client, thick onboard brain. The rover is fully autonomous — a laptop, when present, is only an RViz viewer.
POWER
12 V battery
source
XL4015 buck
→ 5 V / 3 A for Pi
L298N driver
12 V-rated motor stage
MOSFET stage
IRLZ44N + 1N5822 + 1000 µF
E-stop
cuts actuator power only
RASPBERRY PI 4
THE BRAIN · ROS 2 Jazzy
Coverage planner · EKF localisation · CNN classifier · defect mapper · PDF report
USB serial · micro-ROS
ESP32-WROOM-32
THE REFLEXES · micro-ROS client
100 Hz motor PID · encoder ISR counting · solenoid gate · I²S audio capture (<2 ms jitter)
SENSORS & ACTUATORS
2× N20 + encoders
700 ticks/rev → 0.19 mm
12 V solenoid
30 ms strike, rubber tip
INMP441 I²S mic
digital → immune to PWM noise
MPU6050 IMU
yaw for straight rows
VL53L0X ToF
boundary discovery + drift fix
SSD1306 OLED
on-robot status
Notes: Key defence: the Pi cannot do jitter-free 100 ms audio gating because Linux preempts it; the ESP32 cannot run ROS 2 or a CNN. The split IS the architecture.

## Slide 7
HARDWARE JUSTIFICATION
Engineering decisions we can defend
Encoder motors, not the lab BO motors
Encoders ARE the localisation. Without tick counting there is no position, no map — the project reduces to a robot that taps randomly.
Differential drive, not 4-wheel skid steer
Skid steer drags wheels sideways through every turn. That slip corrupts odometry and visibly smears the defect map.
L298N, not DRV8833
The 12 V battery exceeds DRV8833’s 10.8 V absolute maximum. L298N is 12 V-rated; its ~2 V drop lands the motors at a safe ~10 V.
Digital I²S microphone, not analog
An analog electret picks up motor PWM switching noise. I²S output is digital at the sensor — the noise never enters the signal path.
Solenoid, not a servo hammer
A solenoid delivers repeatable impulse energy. Consistent strike energy is what makes tap acoustics comparable between cells.
Local 1000 µF reservoir
The 1 A strike transient is served by local capacitance so the 5 V rail never dips and reboots the Pi mid-scan.
Total build cost ₹3,000 — against commercial acoustic NDT instruments at several lakh rupees.
Notes: Every one of these is a question a reviewer may ask. Knowing why we did NOT choose the obvious alternative is worth more than the choice itself.

## Slide 8
SOFTWARE IMPLEMENTATION
ROS 2 computation graph
One micro-ROS driver node on the ESP32; nine processing nodes on the Pi. Three are managed lifecycle nodes.
ESP32
firmware
(micro-ROS)
publishes
/wheel_ticks
/imu/data_raw
/tof/range
/audio/tap_window
/battery
subscribes
/cmd_vel
serves
/tapper/fire
base_controller
ticks → /odom + TF
LC
ekf_localization
odom ⊕ IMU fusion
boundary_explorer
/discover_area action
coverage_planner
/scan_area action · FSM
LC
tap_scheduler
settle timing, tap retry
surface_classifier
DL-2 · surface type
audio_classifier
DL-1 · MFCC → CNN
LC
defect_mapper
builds the heat map
defect_refiner
DL-3 · region cleanup
report_generator
PDF export
LC = managed lifecycle node (configure → activate) for deterministic, scriptable bring-up
Notes: Point out that node count is not the metric — the reason for the split is. ESP32 holds one node with many interfaces to minimise DDS overhead on a memory-constrained MCU.

## Slide 9
SOFTWARE IMPLEMENTATION
ROS 2 interfaces and engineering depth
TOPICS
/wheel_ticks 50 Hz
/imu/data_raw 100 Hz
/odometry/filtered 50 Hz
/cmd_vel 20 Hz
/audio/tap_window event
/tap/classification event
/defect_grid 1 Hz
/defect_markers event
SERVICES
/tapper/fire
/calibrate_surface
/generate_report
/reset_odom
/estop
ACTIONS
/discover_area
goal: max_len, max_wid
result: L, W
/scan_area
feedback: % complete,
taps done, defects found
result: return_error
QoS differentiation
Sensor streams BEST_EFFORT; audio and classification RELIABLE / KEEP_ALL — losing a tap corrupts the map, losing an IMU packet does not.
TF tree correctness
map → odom → base_link → tapper_link. Taps are stamped at the striker pose, 6 cm ahead of robot centre — otherwise the whole map shifts.
Why NOT Nav2
Nav2 assumes obstacle-rich costmap navigation. On a flat scan surface it is unjustifiable overhead; a purpose-built coverage planner matches the problem.
Notes: Custom interfaces: TapResult.msg, ScanArea.action, DiscoverArea.action in package ss_interfaces. Being able to say why NOT Nav2 scores more than using it decoratively.

## Slide 10
AI IMPLEMENTATION
Where Deep Learning is used — and why
Three models, each solving a problem that rules genuinely cannot. Learning is applied to perception, not to motion control.
DL-1
CORE
Tap Acoustic Classifier
In 100 ms window → MFCC (13 × 9)
Net small CNN, <100 k params, ~2 ms on Pi
Out bonded / debonded + confidence
A single threshold cannot separate the classes — the difference lives in the joint pattern of spectral centroid, decay envelope and resonance peaks, and it shifts with tile type and thickness.
DL-2
SUPPORT
Surface Type Classifier
In 10 calibration taps
Net lightweight classifier on MFCC statistics
Out ceramic / concrete / marble / plaster
A model trained on ceramic tile fails on concrete. DL-2 detects the surface during calibration and loads matching classifier weights — this is what makes TapMap deployable beyond one panel.
DL-3
SUPPORT
Defect Region Refiner
In raw defect occupancy grid
Net compact U-Net-lite over the grid
Out contiguous defect regions + area
Real debonding is spatially contiguous. One red cell surrounded by eight green cells is noise. DL-3 removes isolated false positives and merges scattered hits into coherent regions.
Safety net: a spectral-centroid + decay-time rule classifier ships alongside DL-1 as a fallback — and doubles as the ablation baseline for the paper.
Notes: If asked why navigation is not learned: on a known rectangular grid a learned controller adds training burden and failure modes with zero accuracy gain. Classical control is the correct engineering choice.

## Slide 11
CORE OUTPUT
How the defect heat map is built
1
Grid initialised
A nav_msgs/OccupancyGrid is created over the discovered area — 5 cm cells, origin at the start corner, every cell = −1 (unknown, grey).
2
Pose resolved at the striker
On each classification the mapper does a TF lookup at tapper_link, not base_link. The striker sits 6 cm ahead of centre; using robot centre would shift the entire map.
3
Confidence-weighted write
solid → cell = 0. hollow → cell = round(100 × confidence). The map encodes certainty, not a binary yes/no. Repeat taps are combined as a running average.
4
Two visual layers
/defect_grid renders as the heat map; /defect_markers drops a green or red dot at each individual tap point so the exact strike locations stay visible.
5
DL-3 refinement
The region refiner smooths isolated false positives and merges scattered hits into contiguous defect regions with area estimates.
6
Export
report_generator renders the final grid to PDF with the tap table, spectrograms of flagged cells, total defect area and the return-home error.
LIVE IN RVIZ 2
green = bonded · red = debonded
Directly measured, not interpolated
Every coloured cell was physically struck at that coordinate. Nothing between samples is estimated or diffused — a stronger claim than an interpolated field map.
Notes: This is the slide reviewers will dig into. The tapper_link TF detail and the confidence weighting are the two points that show engineering maturity.

## Slide 12
CURRENT STATUS
Where we are today
✓
ROS 2 Jazzy running on the robot’s onboard Pi 4
Ubuntu 24.04 Server 64-bit flashed, ROS 2 Jazzy installed, headless over SSH. The full tapmap_ws workspace builds and runs on the robot itself — not on a laptop.
✓
Full autonomous scan verified end to end
187 tap points over 0.8 x 0.5 m at 5 cm spacing. 16 defect cells correctly localised over a hollow region the robot was never told about. Returned to origin with 1.47 cm error.
✓
Live defect heat map rendering in RViz 2
Green markers on bonded taps, red block over the debonded region, occupancy grid filling in real time as the rover rasters.
✓
Hardware procured; assembly underway
Pi 4, ESP32, MPU6050, VL53L0X, OLED, L298N and chassis from the lab. Encoder motors, solenoid, INMP441, buck converter and wiring received. Firmware toolchain in setup.
NEXT
Done
Pi flashed · ROS 2 Jazzy · tapmap_ws running onboard
Done
Autonomous scan · heat map · 1.47 cm return error
Now
Chassis assembly · power tree · XL4015 set to 5 V
Wk 1
micro-ROS firmware · encoder ticks · motor PID
Wk 2
Odometry calibration · gate: 2 m out-and-back < 2 cm
Wk 3
Tapper · gated I²S capture · record 600+ taps · DL-1
Wk 4
Boundary discovery · DL-2 · DL-3 · PDF report
Wk 5
Hardening · 5 clean scans · demo · paper draft
Software is ahead of hardware by design — when the parts land we plug them into a stack that already works.
Notes: If they ask to see something running, open the simulation live: ros2 launch tapmap sim.launch.py, then send a scan goal and show RViz.

## Slide 13
LIVE OUTPUT
Verified result — a defect it was never told about
Full autonomous scan on the onboard Raspberry Pi. The rover covered the area, classified every tap, and localised a hollow region that exists only in the simulated panel — it had no prior knowledge of its position.
187
TAP POINTS
0.8 x 0.5 m area at 5 cm grid spacing
16
DEFECT CELLS
spatially matching the planted hollow region
1.47 cm
RETURN ERROR
position error after the full 187-tap scan
0.008 / 0.997
CLASS SEPARATION
band-energy ratio: bonded vs debonded
DEFECT HEAT MAP — RVIZ 2
Green = bonded tap · Red = debonded tap
Every coloured cell was physically struck at that coordinate — nothing is interpolated.
Notes: The return error is the self-audit: if odometry had drifted, the robot would not land within 1.47 cm of its start mark after 187 taps, and every coordinate on the map would be suspect.

## Slide 14
CONTRIBUTION
Why this stands apart
1
First low-cost robotic percussion sounding
Manual tap testing is accepted NDT practice. Automating it with autonomous coverage and spatial mapping has no student-project precedent and almost no low-cost precedent at all.
2
Repeatable strike energy
A solenoid + hardware-gated capture makes taps comparable cell to cell. A human hammer cannot deliver constant impulse energy — this is what makes the acoustics learnable.
3
Self-validating accuracy
The rover returns to origin and reports its own position error. Map trustworthiness is demonstrated, not asserted.
4
Audience-verifiable result
Hand a judge a coin. They tap the panel and hear the hollow spot exactly where the robot marked it. Independently confirmed in five seconds.
5
A dataset that does not exist
A labelled bonded/debonded tap-acoustic dataset is a publishable contribution in its own right.
6
Deployable economics
₹3,000 against several lakh for commercial acoustic NDT — the difference between a lab instrument and something a municipality could actually buy.
Notes: Close on point 4 — the interactive verification. It is the single most memorable thing in the whole project.

## Slide 15
TapMap
Turning a human ear-based safety check into an objective,
repeatable, documented robotic survey.
₹3,000
TOTAL BUILD COST
~150
TAPS PER M²
0.19 mm
ODOMETRY RESOLUTION
3
DEEP LEARNING MODELS
Questions
Notes: Anticipated questions: ambient noise (answer: 100 ms gated capture, tap transient SNR is huge), non-rectangular rooms (future work), why not a camera (no visual signature — the defect is subsurface).